## Slide 1: IP Addressing (Classful & Classless) & Subnetting
Mr. Bhumesh M.

## Slide 2: Roadmap
IP Addressing
Subnet Mask Value
Network Address & Broadcast address
Subnetting
VLSM (Variable Length Subnet Mask)
Supernetting

## Slide 3: IP Addressing
IP Address is a32 bit value
00000000.00000000.00000000.00000000
0 . 0 . 0 . 0
First IP Address
11111111.11111111.11111111.11111111
255 . 255 . 255 . 255
Last IP Address

## Slide 4: IP Addressing
IP address from 0.0.0.0 to 255.255.255.255 are classified into 5 classes based on First octet value.
Class A 0-127
Class B 128-191
Class C 192-223
Class D 224-239
Class E 240-255

## Slide 5: IP Addressing
Class A:
Parity Bit = 0
00000000=0
01111111=127

## Slide 6: IP Addressing
Class B:
Parity Bit = 10
10000000=128
10111111=191

## Slide 7: IP Addressing
Class C:
Parity Bit =110
11000000=192
11011111=223

## Slide 8: IP Addressing
Class D:
Parity Bit =1110
11100000=224
11101111=239

## Slide 9: IP Addressing
Class E:
Parity Bit =1111
11110000=240
11111111=255

## Slide 10: IP Addressing
IP Address has four octets. Every octet contains 8 bits
Octet1 Octet2 Octet3 Octet4
192. 168. 6. 1
11000000.101010000.00000110.00000001

## Slide 11: Subnet Mask Value
Subnet mask value defines properties of IP Address to which it can communicate and to which it can not.
Subnet mask value defines Network component and host component of an IP address.
IP address uses subnet mask to find out boundaries of network.
-Subnet mask value is a driver of IP Address.
Network Bits are always represented with ‘1’
Host Bits are always represented with ‘0’.

## Slide 12: Subnet Mask Structure
CLASS A Subnet Mask Structure
N.H.H.H
11111111.00000000.00000000.00000000
255.0.0.0

## Slide 13: Subnet Mask Structure
CLASS B Subnet Mask Structure
N.N.H.H
11111111. 11111111.00000000.00000000
255.255.0.0

## Slide 14: Subnet Mask Structure
CLASS C Subnet Mask Structure
N.N.N.H
11111111. 11111111. 11111111.00000000
255. 255. 255.0

## Slide 15: Class A Networks
16777214
16777214
16777214
16777214
16777214
16777214
16777214
16777214
16777214
Number of Networks: 126
Number of Hosts per Network: 224 =16777216

## Slide 16: Class B Networks
65534
65534
65534
65534
65534
65534
65534
65534
65534
Number of Networks: 16384
Number of Hosts per Network: 216 =65536

## Slide 17: Class C Networks
254
254
254
254
254
254
254
254
254
Number of Networks: 2097152
Number of Hosts per Network: 28 = 256

## Slide 18: What is Network Address?
Network Address is the identification address for all the systems in the network
The systems with same network address can communicate with each other
Systems with different network addresses can not communicate generally

## Slide 19: What is Broadcast Address?
Broadcast Address is used to deliver a broadcast message to all the computers in the network.
The systems with same network address can have same broadcast address.
All the systems in between Network address and broadcast address form a logical network to communicate with each other.

## Slide 20: Note
Network Address and Broadcast Address are the boundaries of a network. They can't be assigned to computer

## Slide 21: How to find out Network Address?
Identify class of IP Address and Subnet mask Structure.
Replace Host portion with 0 (or)
Perform a logical AND operation between IP Address and subnet mask value.

## Slide 22: How to find out Broadcast Address?
Identify class of IP Address and Subnet mask Structure Replace Host portion with 255 (or)
Perform a logical OR operation between IP Address and inverse subnet mask value
10.185.223.19
N.H.H.H
Network Address= 10.0.0.0
Broadcast Address = 10.255.255.255

## Slide 23
172.20.18.96
N.N.H.H
Network Address = 172.20.0.0 Broadcast Address 172 20.255 255
192.168.6.145
N.N.N.H
Network Address= 192.168.6.0
Broadcast Address= 192.168 6.255

## Slide 24: Class A Networks
10.0.0.1
TO
10.255.255.254
I am Network Address
I am Broadcast Address
We are 16777214 hosts. We can communicate with each other
10.0.0.0
10.255.255,255

## Slide 25: Class B Networks
172.16.0.1
TO
172.16.255.254
I am Network Address
I am Broadcast Address
We are 65536 hosts. We can communicate with each other
172.16.0.0
172.16.255,255

## Slide 26: Class C Networks
192.168.6.1
TO
192.168.6.254
I am Network Address
I am Broadcast Address
We are 16777214 hosts. We can communicate with each other
192.168.6.0
192.168.6,255

## Slide 27: IP Addressing
Class | Parity | Range | Subnet Mask Structure | Subnet Mask Value | Networks | Host Per Network
A | 0 | 0-127 | N.H.H.H | 255.0.0.0 | 126 | 16777214
B | 10 | 128-191 | N.N.H.H | 255.255.0.0 | 16284 | 65534
C | 110 | 192-223 | N.N.N.H | 255.255.255.0 | 2097152 | 254
D | 1110 | 224-239 | Multicasting - Video Conference |  |  | 
E | 1111 | 240-255 | Reserved by IETF-for R&D |  |  | 

## Slide 28
Chart: 
| A | B | C | D | E
IP Address Percentage | 0.5 | 0.25 | 0.125 | 0.0625 | 0.0625

## Slide 29: IP Address Related organizations
IANA - Internet Assigned Numbers Authority
ICANN- Internet Corporation for Assigned Numbers and Names
Types of IP Addresses
Private IP Addresses
Public IP Addresses
Special IP Addresses

## Slide 30: Private IP Addresses
The IP addresses not routable in public network
Used to communicate within private network.
Internet access is not possible with private IP address
Defined in RFC 1918
CLASS A | 10.0.0.0 / 8 | 10.0.0.0 – 10.255.255.255
CLASS B | 172.16.0.0 / 12 | 172.16.0.0 – 172.31.255.255
CLASS C | 192.168.0.0 / 16 | 192.168.0.0 – 192.168.255.255

## Slide 31: Special IP Addresses
0.0.0.0 Network is reserved for default routing. Can't be assigned to systems
127.0.0.0 Network is reserved for loop back purpose (NIC diagnosis)
Class D Networks are reserved for multicasting. Not for systems
Class E Networks are reserved for Research and Development. Not for systems

## Slide 32: SUBNETTING
What is Subnettin9?
Logically breaking the major network into smaller networks Subnets.
Advantage of Subnetting
*Reduce wastage of IP Addresses
(Once the network is used, it can't be used again in the same organization)
Subnetting Procedure
Increase network bits in the subnet mask value from left to right

## Slide 33: 192.168.6.0 Subnetting
256
1111111111.11111111.11111111.00000000 255.255 255.0
128 | 128
11111111.11111111.11111111.10000000 255 255 255.128 | 
64 | 64 | 64 | 64
11111111.11111111.11111111 11000000 255.255.255. 192 |  |  | 
32 | 32 | 32 | 32 | 32 | 32 | 32 | 32
11111111.11111111.11111111.11100000 255.255.255.224 |  |  |  |  |  |  | 

## Slide 34: Subnetting Formulae
No of Networks 2N N= increased Network bits
No of Hosts per Network- 2N- 2 H=remaining Host bits

## Slide 35: Example to understand Formulae
192.168.6.0 Subnetting: 3 Network bits increased.
32 | 32 | 32 | 32 | 32 | 32 | 32 | 32
11111111.11111111.11111111.11100000 255.255.255.224 |  |  |  |  |  |  | 
N=3 No of Networks = 2N = 23 = 8
H=5 No of Hosts per Network = 2H – 2 = 25 = 32-2 = 30

## Slide 36: Subnetting Methods
Subnetting can be done in two ways
Based on No of Networks
Based on No of Hosts

## Slide 37: SUBNETTING Calculations
Based on No of Networks:
Identify required No of subnets.
Refer 2 power chart.
Identify N value.
Increase the bits in the subnetmask value.
Identify H value.
Find out new subnet mask value.
Find out No of subnets and No of hosts.
Subtract new subnet mask value from 255.255.255.255.
Find out network address & Broadcast address of all subnets.

## Slide 38: Based on No of Hosts:
Identify required No of Hosts per subnet.
Refer 2 power chart.
Identify H value.
Increase the bits in the subnetmask value.
Identify N value.
Find out new subnet mask value.
Find out No of subnets and No of hosts.
Subtract new subnet mask value from 255.255.255.255.
Find out network address & Broadcast address of all subnets.

## Slide 39: Based on No of Networks
Q1. Divide 192.168.6.0 into 4 subnets
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
255.255.255.0
11111111.11111111.11111111.110000000
255.255.255. 192
N=2 H=6
No of Networks = 2N = 4
No of Hosts per Network= 2H – 2 = 62

## Slide 40: Continue….
 | Network Address | Broadcast Address
Subnet 1 | 192.168.6.0 | 192.168.6.63
Subnet 2 | 192.168.6.64 | 192. 168..127
Subnet 3 | 192.168.6.128 | 192.168.6.191
Subnet 4 | 192.168.6.192 | 192.168.6.255
255.255.255.255
255.255.255.192
0.0.0.63

## Slide 41: Based on No of Networks
Q1. Divide 10.0.0.0 into 100 subnets
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
255.0.0.0
11111111.11111110.00000000.000000000
255.254.0. 0
N=7 H=17
No of Networks = 2N = 128 (use 100)
No of Hosts per Network= 2H – 2 = 1310170

## Slide 42: Continue….
 | Network Address | Broadcast Address
Subnet 1 | 10.0.0.0 | 10.1.255.255
Subnet 2 | 10.2.0.0 | 10.3.255.255
Subnet 3 | 10.4.0.0 | 10.5.255.255
Subnet 4 ---------- | 192.168.6.192 ------------------- | 192.168.6.255 --------------------
Subnet 127 | 10.252.0.0 | 10.253.255.255
Subnet 128 | 10.254.0.0 | 10.255.255.255
255.255.255.255
255.254.0.0
0.1.255.255

## Slide 43: Based on No of Networks
Q1. Divide 172.16.0.0 into 64 subnets
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
255.255.0.0
11111111.11111111.11111100.000000000
255.255.252. 0
N=6 H=10
No of Networks = 2N = 64
No of Hosts per Network= 2H – 2 = 1022

## Slide 44: Continue….
 | Network Address | Broadcast Address
Subnet 1 | 172.16.0.0 | 172.16.3.255
Subnet 2 | 172.16.4.0 | 172.16.7.255
Subnet 3 | 172.16.8.0 | 172.165.11.255
Subnet 4 ---------- | 172.16.12.0 ------------------- | 172.16.15.255 --------------------
Subnet 127 | 172.16.248.0 | 172.16.251.255
Subnet 128 | 172.16.252.0 | 172.16.255.255
255.255.255.255
255.255.252.0
0.0.3.255

## Slide 45: Based on No of Hosts
Q1. Divide 192.168.6.0 into subnets with 28 hosts
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
255.255.255.0
11111111.11111111.11111111.111000000
255.255.255.224
N=3 H=5
No of Networks = 2N = 8
No of Hosts per Network= 2H – 2 = 30

## Slide 46: Continue….
 | Network Address | Broadcast Address
Subnet 1 | 192.168.6.0 | 16192.8.6.31
Subnet 2 | 192.168.6.32 | 192.168.6.63
Subnet 3 | 192.168.6.64 | 192.168.6.95
Subnet 4 | 192.168.6.96 | 192.168.6.127
Subnet 5 | 192.168.6.128 | 192.168.6.159
Subnet 6 | 192.168.6.160 | 192.168.6.191
Subnet 7 | 192.168.6.192 | 192.168.6.223
Subnet 8 | 192.168.6.224 | 192.168.6.255
255.255.255.255
255.255.255.224
0.0.0.31

## Slide 47: Based on No of Hosts
Q1. Divide 10.0.0.0 into subnets with 4000 hosts
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
255.0.0.0
11111111.11111111.11110000.00000000
255.255.240.0
N=12 H=12
No of Networks = 2N = 4096
No of Hosts per Network= 2H – 2 = 4094

## Slide 48: Continue….
 | Network Address | Broadcast Address
Subnet 1 | 10.0.0.0 | 10.0.15.255
Subnet 2 | 10.0.16.0 | 10.0.31.255
Subnet 3 | 10.0.32.0 | 10.0.47.255
Subnet 4 | 10.0.48.0 | 10.0.63.255
------------ | ----------------- | -------------------
Subnet 4094 | 10.255.208.0 | 10.255.223.255
Subnet 4095 | 10.255.224.0 | 10.255.239.255
Subnet 4096 | 10.255.240.0 | 10.255.255.255
255.255.255.255
255.255.240.0
0.0.15.255

## Slide 49: Question.
Q.3 Divide 172.16.0.0 into subnets with 500 hosts

## Slide 50: VLSM
Variabie Lengh Subnet Mask.
Also called as Subnettimg of Subnetting.
Subnetting is used to break the network equally.
If these networks are Subnetted again, different subnets may have different subnet mask values, also called as Variable length subnet masks.
With VLSM, 1P addressing scheme is used more efficiently without wastage.

## Slide 51: VLSM Example

## Slide 52: Supernetting
What is Supernetting?
This is reverse procedure of Subnetting.
It is used to combine the networks/ subnetworks
To combine the networks decrease the network bits from right to left.
Generally Supernètting concept is used in router advertisements, called as route summarization
Supernetting calculations are similar to Subnetting calculations

## Slide 53: Continue..
192.168.0.0 /24 | 192.168.1.0 /24 | 192.168.2.0 /24 | 192.168.3.0 /24
192.168.0.0 /23 |  | 192.168.0.0 /23 | 
192.168.0.0 /22 |  |  | 

## Slide 54
Any questions??

## Slide 55
Thank You!!!!!!!!