## Slide 1: IPV6 (Internet Protocol version 6)
Mr. Bhumesh M.

## Slide 2: What is IPv6?
Internet Protocol version 6 (Also called as IPng - IP next generation).
IPv4 addressing scheme has 4294967296 IP addresses.
IPv4 addresses are not enough in future with Internet evolution.
IPv6 is introduced as IPv4 addresses are being saturated.
IPv6 is 128 bit, Hexadecimal notation.

## Slide 3: Differences between IPv4 and IPv6
IPv4 | IPv6
Internet Protocol version 4 | Internet Protocol version 6
32 bit value | 128 bit value
44294967296 ip addresses | 3.4 x 1038 IP addresses
Dotted decimal notation | Hexadecimal notation (string notation)
192.168.6.1 | 2000:58ab:0000:0000:12cd:0011:8901:13fd
Uses unicast, multicast, broadcast | Uses unicast, multicast, any Cast
Classified into A B C D E classes | No classifiCation

## Slide 4: IPv6 Features
very large Address space:
IPv6 has 3.4 x 1038 IP addresses. with IPv6 every device in every house can have IP address.
Security:
IPSec is in built into IPv6. Two devices can dynamically negotiate security parameters and build a secure tunnel between them with no user intervention.
Mobility:
With the growth of mobile devices, such as PDAs and smart phones, devices can roam between wireless networks without breaking their connectivity

## Slide 5
Streamlined encapsulation:
IPv6 encapsulation is simpler than IPv4, providing faster forwarding rates by routers and better routing efficiency. No checksum is included in IPv6 header.
Transition capabilities:
Various solutions exist to allow IPv4 and iPv6 to successfully coexist when migrating between the two

## Slide 6: IPv6 addressing scheme:
First IPv6 Address:
0000 O000 CO00 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 00000000 00CO 0000 000 0000 000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000:0000:0000:0000:0000:0000:0000:0000
Last IPv6 Address:
1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 11111111 111T 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111
FFFF:FFFF:FFFF: FFFF: FFFF:FFFF:FFFF: FFFF

## Slide 7: IPv6 addressing scheme- simplification:
A leading zero in a set of numbers can be omitted.
Successive fields of zeroes are replaced with : but only once if it is used more than once, it leads to confusion to identify set of zeroes
An unspecified address is represented with :: since it contains all zeroes.
1200:5600:0028: afcd:0004:0589:0009:ca39 1200:5600:28:afcd:4:589:9:ca 39
2000:0001:0000:0000:0000:000c:00ea: 00002000:1:0:0:0:c: ea:02000:1::c:ea:0
0000:0000:0000:0000:0000:0000:0000:0000

## Slide 8: Types of IPv6 Addresses
Unicast
One to one interface (same as IPv4)
Multicast
One to a group of devices (same as IPv4)
Anycast
One to nearest interface, where many interfaces can share the same address
No Broadcast exists in IPv6
:: is unspecified address that is 0000:0000:0000:0000:0000:0000:0000:0000 :: 1 is loop back address that is CO00:0009:0000:0000:0000:0000:0000:0001

## Slide 9: Unicast
One to one interface communication
Private IPv6 addresses (FE80::/10)
IP addresses are used for devices that don't need to access
public network.
Two kinds of private addresses:
Site-local FEC:: through FEF :: (locally specific in the LAN)
Link-local FE8::through FE8 :: (locally specific on the link)
Global/public IPV6 addresses : (2000::/3)
IP addresses are used for devices that need to access a public network
IANA has currently assigned only 2000::/3 addresses to the global pool, which is about 1/6th of the available IPv6 addresses.

## Slide 10: Multicast
One to group of devices communication
FF::/8 is the address range
First 8 bits are set to FF
Next 4 bits are the lifetime of the address: 0 is permanent and 1 is temporary.
Next 4 bits indicate scope of the multicast address (Eg: 1 is for a node, 2 is for a link, 5 is for the site, 8 is for the organization, and E is global, the internet)
For example:
FFO2::/16 is a permanent link address
FF15::/16 is a temporary address for a site

## Slide 11: Anycast
One to nearest interface.
Anycast address identifies one or more interfaces.
Anycast is a hybrid of unicast and multicast address.
A packet is sent to any one member of a group of devices that are configured with the anycast address.
By default packets sent to an anycast addresses are forwarded to the closest interface.
Anycast address is also known as one-to-the-nearest address.
Anycast addresses are allocated from the global pool of unicast addresses in IPv6.

## Slide 12: Anycast
It is difficult to distinguish between unicast and anycast as they use common address Space.
Don't assign anycast addresses to hosts.
Anycast addresses can be assigned to routers.
Don't put anycast address in the source of a packet- only the destination.
Anycast addresses and their uses are still in their infancy and some known problems can occur when using them.

## Slide 13: IPv6 Address Structure
16 | 23 | 32 | 48 | 64 | 80 | 96 | 112 | 128
2001 |  |  |  |  | EUI - 64 |  |  | 
Registry-- |  |  |  |  | --------INTERFACE ID------------------- |  |  | 
ISP Prefix ------- |  |  |  |  |  |  |  | 
Site Prefix -------------------- |  |  |  |  |  |  |  | 
Subnet Prefix ----------------------------- |  |  |  |  |  |  |  | 
--------SUBNET ID---------------------- |  |  |  |  |  |  |  | 

## Slide 14: IPV6 Address structure Assignment
IANA has assigned only 2000:/3 addresses to the global pool of these addresses, only 2001::/16 are assigned to various Internet address registries.
Global Unicast addresses are made up of two components
Subnet ID (64 bits)
Interface ID (EUI -64 Dits)
Subnet ID contains:
The Registry (which is responsible for assigning it ,such as IANA)
The ISP prefix (which ISP is associated with the address)
The site prefix (Which company is associated with the address)
The subnet prefix (subnets within the site)
Interface ID is EUI-64:
EUI-64 Extended unique identifier 64 (EUl-64)

## Slide 15
IPv6 address can be assigned in three ways
Static IP (specify all 128-bits manually)
Dynamic IP (through DHCP server)
EUI- 64 (stateless auto configuration)
IPv6 15 auto configurable with EUl-64 as interface ID.
EUI-64 is obtained by inserting FF FE in between MAC address of the system to fulfill 64 bits.

## Slide 16
OUI | NIC ID
OUI | FF | FE | NIC ID
MAC ADDRESS
EUI - 64

## Slide 17: Routers with IPv6
Enable IPv6 routing:
Router(config)# ipv6 unicast-routing
Assigning IPv6 address to interface:
Router(config)# interface fa 0/1
Router(config-if)# ipv6 address 2001:1cc1:dddd:2::/64 eui-64
Routing protocols for IPv4 and IPv6:
IPv4 Routing Protocols | IPV6 Routing Protocols
RIP | RIPng (RIP new generation)
OSPF | OSPFv3
EIGRP | EIGRP for ipv6

## Slide 18: IPv4 to IPv6 transition options:
Dual stacking
Manual IPv6-over-IPv4 (6 to 4) tunneling.
Dynamic 6 to 4 tunneling.
Intra-Site-Automatic tunnel addressing protocol tunneling (ISATAP)
Teredo tunneling
NAT Proxying and Translation (NAT- PT)

## Slide 19
Thank You!!!!!!!!